## Slide 1: CBETA bunch pattern and BPM trigger generator Version 2
R. Michnoff, J. Dobbins, R. Hulsart
February 4, 2019

## Slide 2
Clock input
(41.9 MHz)
n
R[7..0]
Pattern Repeat Clock
(41.9 MHz / R)
Divide by n
R typically =
44 or 88
n
Divide by n
N[23..0]
Injection Start Clock
(as low as 1 Hz)
z
Delay by Z
Z[7..0]
CLK
START
CLK
M[18..0]
Trigger pattern count
R[7..0]
Injection Start Clock Delayed
by Z 41.9 MHz periods
(to be selected as optional output instead of Inj Start Clk
To LASER
OEM
LASER Trigger Pattern Generator
START
CLK
BPM Trigger
Trigger 1
Number of total triggers
Trigger pattern
P[127..0]
Reset
Done
Reset
Mode
Mode
Trigger Mode
0: One trigger on START
1: One trigger for each trigger pattern cycle until Reset
Trigger Pattern
The trigger pattern will be implemented as a shift register for the output trigger.
When a START pulse is received, the trigger pattern register P is shifted to the output (bit 0 first) until R triggers have occurred. Then the trigger pattern repeats.
After a total number of M triggers are generated the Done output is asserted which halts and resets the pattern generator and all triggers.
IN
OUT
Period (seconds)
LASER Trigger Limiter
T[16..0]
Max trigger cnt
C[31..0]
z
Delay by Z1
Z1[7..0]
CLK
Laser Trigger Limiter
Halt triggers if C triggers is exceeded during T second period. Allow triggers again after T seconds expires
START
CLK
Trigger 2
Trigger 2
Reset
Mode
Mode
z
Delay by Z2
Z2[7..0]
CLK
Trigger pattern count
Trigger pattern count
Enable
Enable/Disable