## Slide 1: OSC simulation update
Suntao Wang
10/06/2017

## Slide 2
Transit-time optical stochastic cooling (TTOSC)
Particle receives the energy kick dp/p from the kicker undulator:
where x0 is the amplitude, k=2p/l,
M5n are the elements of the 6x6 transfer matrix from the pickup undulator to the kicker undulator, (x, qx, Dp/p) are the particle horizontal coordinate, angle, and relative momentum deviation in the pickup.
g: Optical amplifier gain
q: electron charge
e0: EM wave amplitude of the light from the pickup
Nu: number of kicker undulator periods
lu: the period length of the kicker undulator
K: the pickup undulator K parameter
Eb: electron beam energy
g: 948 @ 500MeV
In simulation, x0 is one parameter

## Slide 3
Single element test: 100 particles, track for 50 turns, excitation and damping turned on
Normal emittance are extracted from the sigma matrix every turn
Q45E: large horizontal dispersion 2.05 m in the test lattice (2.1GeV CesrTA lattice)
M51: -1.35E-7, M52=1.26E-6, M56= 3E-8,
undulator light wavelength: l=1 mm, gain: x0=1E-2
Each particle receives the energy kick based on its own (x, x’, z’)
Only horizontal emittance reduced. The energy spread and bunch length slight increased.

## Slide 4
Single element test: 100 particles, track for 50 turns, excitation and damping turned on
Q45E: large horizontal dispersion 2.05 m in the test lattice (2.1GeV CesrTA lattice)
M51: -1.35E-7, M52=1.26E-6, M56= 1E-6,
undulator light wavelength: l=1 mm, gain: x0=1E-2
Each particle receives the energy kick based on its own (x, x’, z’)
Both horizontal and longitudinal emittance reduced. The energy spread reduced either.

## Slide 5
Now the particle receives a energy kick based on the average x position in a slice.
z
x
Slices based on the particles longitudinal position z
N_slice= 62
Slice_width = 1 mm
When using slice x position, the cooling rate reduced.

## Slide 6
Simple line test:
Q48W
Q48E
Und_pick
Und_kick
In tracking simulation at each turn:
Record the particle distribution in z at the end of Und_pick
Particle receive the energy kick at the end of Und_kick
M51: -3.09E-5, M52=9.47E-5, M56= 7.6E-7,
undulator light wavelength: l=1 mm, gain: x0=3E-3
Cooling depends on the gain.

## Slide 7: Summary:
Based on the TTOSC principle, simulation shows the cooling seems to work.
Will incorporate MPE’s bypass line into CESR lattice for simulation test